## Slide 1: Transfer ASIC design to Palladium emulator
For Chip emulation &
Simulation Acceleration

## Slide 2: What is the Palladium emulator?
The Palladium emulator is a unique machine, that can run a logic design much faster than the simulation, and still keeps all the signals & logic elements visible.
We use Palladium in two ways:
  The Palladium runs fast enough to be connected to lab equipment (Emulation).
  To speed up the simulation process and with the simulation environment (Simulation Acceleration).

## Slide 3: Before loading a new design in the Palladium
A module that we want to run on the Palladium have to first work on regular simulation. Also we need to have this simulation so we’ll knew how this module supposed to work, so when it doesn’t work this way the problem can only come from the difference between the simulation and the Palladium.
The main problems expected are:
  Clocks: the clocks in the Palladium are generated by special clock generators. We have to knew how many clocks we have in the design, what are their frequencies, and how they are running in the design.
  Clock gates: some times we have clock gates in the design. Sometimes we get those block from the FUB and they are not synthesizable. We need to check them, and if needed replace them with a synthesizable module.
  RAM’s : The RAM’s module used in simulation are Verilog modules provided by the FUB they are not synthesizable! We need to replace them with synthesizable module.
  Analog modules: most of the times those are behavioral modules that again can’t by synthesize. We need to replace them with synthesizable modules or bypass them.

## Slide 4: Adding Specman to get Simulation Acceleration
The Specman environment will need to get some changes to run on the Palladium. But the top level must stay the same so the test running on the Palladium will be identical to the tests running on the ‘official’ simulation.
The main changes need to by done on the Specman environmen are:
  Events: Specman environment are working from an event to event. In regular Specman environment we can use as much events as we like and as often as we like. So we some time us event even on the clock signal. In the Palladium the Palladium have to stop for each event transfer control to the UNIX for the Specman method and start running again. This will make the simulation very slow almost the speed of regular simulation. So in Palladium SA we need to consider every event we use and use only the major ones.
  Signals: In regular Specman environment we have no limitation on signals we can use or read in the design. In Palladium every domain have only a number of signal that can be used for this we again need to consider which ones we can us and which we can do without. But we can use a Verilog module in the Palladium to replace the signals we can’t use in the environment.
  Memories: we can’t read or write memories in the design with the specman at all (not enough signals). So reading & writing form the Palladium by the Specman must be done through the UNIX environment.

## Slide 5: The palladium compile stages compilation
The first stage is compiling the Verilog code into the Palladium emulator. This is not as easy as it sounds because:
This is the first time the Verilog code is being transfer to an elements net-list.
  Modules written not according to the methodology - the synthesis can’t find logic elements to translate it.
  Code with simulations instructions (assertions, #, $time, $display et’c)
Some of the modules are behavioral modules of analog blocks.
  Need to be replace with synthesizable code or empty and generate the outputs from the simulation part of the Palladium design. (memory's, PLL, Serdes, etc’).
Test Bench; we need a complete new Test Bench.
  Connecting & controlling internal signals from the TB.
  Defining external modules to support the design (FLASH memory, DDR, etc’)
  Making connections to the outside world.

## Slide 6: The palladium compile stages Specman Compilation
If the in the code part there was a chance of things work on compilation. The Specman part will probably compile faster but will work much slower.
At this stage we don’t stop for this our main objective now is to get ALL the design in to ‘feel’ the size. So each module we have problems with will be empty, marked and we’ll deal with it later when we start working the design.

## Slide 7: The palladium compile stages the compiled design
Now we have two ‘clouds’ that still doesn’t work. We have to find data paths and follow them to see that the design is functional.
DUT
SYS.e

## Slide 8: The palladium compile stages the clocks in the design
All clocks in the Palladium emulator are generated by the Palladium system in the Test Bench.
The external (slow) clocks will be generated in the TB and connected to external chips pins.
The internal (fast) clocks will also be generated in the TB but they will be connected to the PLL outputs inside the design.
DUT
PLL
Slow clock
Fast clock

## Slide 9: The palladium compile stages the reset machine
The reset machine is the first RTL code that we work. There is no apparent reason why this would work like in the simulation but:
Some time we have clock gates in the design that are analog and may not work in the Palladium so we can check the signals going in and out to see that they match the simulation. If we found a clock gate and fix it, it will be fixed to the rest of the design.
The times in the Palladium will be different from the simulation so we have to check the design behavior and not relay on time measure.
It has no software and very few controls from the TB (if any). So this will be an easy place to start using specman event_port. But they are not mandatories in this stage.
reset
DUT
Slow clock
Fast clock
Clock gate

## Slide 10: Make_Saenv.csh
##!/usr/local/bin/csh
source synthScripts/setup
if ($#argv < 1) then
echo "Please add directory name"
else
echo "new compilation directory $1"
\rm -rf $1
mkdir $1
cp synthScripts/* $1/.
cd $1
date
source setup
source make_SA_model.csh |tee make_SA_model.log
if($?) then
echo Error on compilation
exit 1
endif
source ../workFiles/make_run_dir.csh
date
echo MELLANOX_STAGE_End
echo "coffee |_P ?"
endif

## Slide 11: Make_SA_model.csh (load files - vlan)
##!/usr/local/bin/csh
date
cp synthScripts/* $1/.
echo MELLANOX_STAGE I Yaron environment vlan
vlan -sv -f compile_inputs.tcl +rtlCommentPragma +tran_relax
if($?) then
echo Error on Vlan
exit 1
endif
date
echo MELLANOX_STAGE II new environment vlan
vlan -sv -f verilog_inputs.tcl +rtlCommentPragma +tran_relax
if($?) then
echo Error in new environment
exit 1
Endif

## Slide 12: Make_SA_model.csh (cont) (synthesis & module compilation – IXCOM)
date
echo MELLANOX_STAGE III ixcom synthsis
ixcom -top external_bfms -top specman_hdl_ref -ua +dut+external_bfms+specman_hdl_ref +xcDesignTop+top.dut=external_bfms +ignoreNCVerCheck -timescale 100ps/100ps -target hdlice -log ixcom_synt.log +tran_relax +targetTop+external_bfms +1xua
if($?) then
echo Error on Ixcom synthsis
exit 1
endif
date
echo MELLANOX_STAGE III ixcom compilation
ixcom -xecompile compilerOptions=compilerOptions.qel +targetTop+external_bfms -log ixcom_comp.log +ignoreNCVerCheck -target xecompile
if($?) then
echo Error on Ixcom compilation
exit 1
endif

## Slide 13: Make_SA_model.csh (cont) (adding external files – irun)
date
echo MELLANOX_STAGE IV irun
irun -c ${ORGDIR}/verilog/top.v patch.e -f xc_work/irun.f -sntimescale 100ps/100ps -timescale 100ps/100ps -top top -sv -clean
if($?) then
echo Error on irun
exit 1
endif

## Slide 14: Make_run_env.csh
##!/usr/local/bin/csh
\rm -rf run_SA_dir
mkdir run_SA_dir
cd run_SA_dir
ln -s ../.design
ln -s ../PLU
ln -s ../CONDOR
ln -s ../WORK
ln -s ../QTDB
ln -s ../PDB
ln -s ../tmp
ln -s ../cellList
ln -s ../dbFiles
ln -s ../xc_work
ln -s ../AxisWork
ln -s ../INCA_libs
cp ../../runFiles/* .
echo "To run Palladium use: irun -R -xedebug -gui -64 -input run_inputs.tcl"