## Slide 1: Simulation Acceleration tutorial
of ASIC design on a Palladium platform

## Slide 2: What do we need?
To make the transaction from regular simulation to Palladium Simulation Acceleration faster, we need to have full knowledge on the design & details of the way this chip preform its function.
  Hardware :
    Modules blocks; we have to have the block diagram of the chip, and approximation of the size of each block.
    Clock & reset; We need to knew the clock & reset trees inside the chip and how are we going to connect this in the Palladium.
    Memories; we need to have a memory module that can work on the Palladium, and replace the memory modules used in simulation.
    Analog blocks; we need to knew which blocks are analog, and what we need to replace them with.
  Specman
    Signals from Specman to Palladium; in simulation we can read & write each signal in the design. In Palladium we have a limit (per board or domain) on those signal so we needs to consider each signal.
    events;The Specman environment works from event to event. In regular simulation we can have as many event as we like, and as often as we like(clocks). When Palladium trigger an event it stop the fast simulation move to the control UNIX for the Specman method and back. If the event are to close this will reduce the speed to ineffective speed. We have to use only major events and may need a Verilog module in the Palladium environment to gather the data and send it to the Specman on one event.
    Memories; memories can’t be written or read. We’ll need to do this some other way.

## Slide 3: Make_Saenv.csh
##!/usr/local/bin/csh
source synthScripts/setup
if ($#argv < 1) then
echo "Please add directory name"
else
echo "new compilation directory $1"
\rm -rf $1
mkdir $1
cp synthScripts/* $1/.
cd $1
date
source setup
source make_SA_model.csh |tee make_SA_model.log
if($?) then
echo Error on compilation
exit 1
endif
source ../workFiles/make_run_dir.csh
date
echo MELLANOX_STAGE_End
echo "coffee |_P ?"
endif

## Slide 4: Make_SA_model.csh (load files - vlan)
##!/usr/local/bin/csh
date
cp synthScripts/* $1/.
echo MELLANOX_STAGE I Yaron environment vlan
vlan -sv -f compile_inputs.tcl +rtlCommentPragma +tran_relax
if($?) then
echo Error on Vlan
exit 1
endif
date
echo MELLANOX_STAGE II new environment vlan
vlan -sv -f verilog_inputs.tcl +rtlCommentPragma +tran_relax
if($?) then
echo Error in new environment
exit 1
Endif

## Slide 5: Make_SA_model.csh (cont) (synthesis & module compilation – IXCOM)
date
echo MELLANOX_STAGE III ixcom synthsis
ixcom -top external_bfms -top specman_hdl_ref -ua +dut+external_bfms+specman_hdl_ref +xcDesignTop+top.dut=external_bfms +ignoreNCVerCheck -timescale 100ps/100ps -target hdlice -log ixcom_synt.log +tran_relax +targetTop+external_bfms +1xua
if($?) then
echo Error on Ixcom synthsis
exit 1
endif
date
echo MELLANOX_STAGE III ixcom compilation
ixcom -xecompile compilerOptions=compilerOptions.qel +targetTop+external_bfms -log ixcom_comp.log +ignoreNCVerCheck -target xecompile
if($?) then
echo Error on Ixcom compilation
exit 1
endif

## Slide 6: Make_SA_model.csh (cont) (adding external files – irun)
date
echo MELLANOX_STAGE IV irun
irun -c ${ORGDIR}/verilog/top.v patch.e -f xc_work/irun.f -sntimescale 100ps/100ps -timescale 100ps/100ps -top top -sv -clean
if($?) then
echo Error on irun
exit 1
endif

## Slide 7: Make_run_env.csh
##!/usr/local/bin/csh
\rm -rf run_SA_dir
mkdir run_SA_dir
cd run_SA_dir
ln -s ../.design
ln -s ../PLU
ln -s ../CONDOR
ln -s ../WORK
ln -s ../QTDB
ln -s ../PDB
ln -s ../tmp
ln -s ../cellList
ln -s ../dbFiles
ln -s ../xc_work
ln -s ../AxisWork
ln -s ../INCA_libs
cp ../../runFiles/* .
echo "To run Palladium use: irun -R -xedebug -gui -64 -input run_inputs.tcl"