## Slide 1: Transfer ASIC design to Palladium emulator
For Chip emulation &
Simulation Acceleration

## Slide 2: What is the Palladium emulator?
The Palladium emulator is a unique machine, that can run a logic design much faster than the simulation, and still keeps all the signals & logic elements visible.
We use Palladium in two ways:
  The Palladium runs fast enough to be connected to lab equipment (Emulation).
  To speed up the simulation process and with the simulation environment (Simulation Acceleration).

## Slide 3: Before loading a new design in the Palladium
A module that we want to run on the Palladium have to first work on regular simulation. Also we need to have this simulation so we’ll knew how this module supposed to work, so when it doesn’t work this way the problem can only come from the difference between the simulation and the Palladium.
The main problems expected are:
  Clocks: the clocks in the Palladium are generated by special clock generators. We have to knew how many clocks we have in the design, what are their frequencies, and how they are running in the design.
  Clock gates: some times we have clock gates in the design. Sometimes we get those block from the FUB and they are not synthesizable. We need to check them, and if needed replace them with a synthesizable module.
  RAM’s : The RAM’s module used in simulation are Verilog modules provided by the FUB they are not synthesizable! We need to replace them with synthesizable module.
  Analog modules: most of the times those are behavioral modules that again can’t by synthesize. We need to replace them with synthesizable modules or bypass them.

## Slide 4: Adding Specman to get Simulation Acceleration
The Specman environment will need to get some changes to run on the Palladium. But the top level must stay the same so the test running on the Palladium will be identical to the tests running on the ‘official’ simulation.
The main changes need to by done on the Specman environmen are:
  Events: Specman environment are working from an event to event. In regular Specman environment we can use as much events as we like and as often as we like. So we some time us event even on the clock signal. In the Palladium the Palladium have to stop for each event transfer control to the UNIX for the Specman method and start running again. This will make the simulation very slow almost the speed of regular simulation. So in Palladium SA we need to consider every event we use and use only the major ones.
  Signals: In regular Specman environment we have no limitation on signals we can use or read in the design. In Palladium every domain have only a number of signal that can be used for this we again need to consider which ones we can us and which we can do without. But we can use a Verilog module in the Palladium to replace the signals we can’t use in the environment.
  Memories: we can’t read or write memories in the design with the specman at all (not enough signals). So reading & writing form the Palladium by the Specman must be done through the UNIX environment.

## Slide 5: Make_Saenv.csh
##!/usr/local/bin/csh
source synthScripts/setup
if ($#argv < 1) then
echo "Please add directory name"
else
echo "new compilation directory $1"
\rm -rf $1
mkdir $1
cp synthScripts/* $1/.
cd $1
date
source setup
source make_SA_model.csh |tee make_SA_model.log
if($?) then
echo Error on compilation
exit 1
endif
source ../workFiles/make_run_dir.csh
date
echo MELLANOX_STAGE_End
echo "coffee |_P ?"
endif

## Slide 6: Make_SA_model.csh (load files - vlan)
##!/usr/local/bin/csh
date
cp synthScripts/* $1/.
echo MELLANOX_STAGE I Yaron environment vlan
vlan -sv -f compile_inputs.tcl +rtlCommentPragma +tran_relax
if($?) then
echo Error on Vlan
exit 1
endif
date
echo MELLANOX_STAGE II new environment vlan
vlan -sv -f verilog_inputs.tcl +rtlCommentPragma +tran_relax
if($?) then
echo Error in new environment
exit 1
Endif

## Slide 7: Make_SA_model.csh (cont) (synthesis & module compilation – IXCOM)
date
echo MELLANOX_STAGE III ixcom synthsis
ixcom -top external_bfms -top specman_hdl_ref -ua +dut+external_bfms+specman_hdl_ref +xcDesignTop+top.dut=external_bfms +ignoreNCVerCheck -timescale 100ps/100ps -target hdlice -log ixcom_synt.log +tran_relax +targetTop+external_bfms +1xua
if($?) then
echo Error on Ixcom synthsis
exit 1
endif
date
echo MELLANOX_STAGE III ixcom compilation
ixcom -xecompile compilerOptions=compilerOptions.qel +targetTop+external_bfms -log ixcom_comp.log +ignoreNCVerCheck -target xecompile
if($?) then
echo Error on Ixcom compilation
exit 1
endif

## Slide 8: Make_SA_model.csh (cont) (adding external files – irun)
date
echo MELLANOX_STAGE IV irun
irun -c ${ORGDIR}/verilog/top.v patch.e -f xc_work/irun.f -sntimescale 100ps/100ps -timescale 100ps/100ps -top top -sv -clean
if($?) then
echo Error on irun
exit 1
endif

## Slide 9: Make_run_env.csh
##!/usr/local/bin/csh
\rm -rf run_SA_dir
mkdir run_SA_dir
cd run_SA_dir
ln -s ../.design
ln -s ../PLU
ln -s ../CONDOR
ln -s ../WORK
ln -s ../QTDB
ln -s ../PDB
ln -s ../tmp
ln -s ../cellList
ln -s ../dbFiles
ln -s ../xc_work
ln -s ../AxisWork
ln -s ../INCA_libs
cp ../../runFiles/* .
echo "To run Palladium use: irun -R -xedebug -gui -64 -input run_inputs.tcl"