## Slide 1: Verification services
To get a cleaner chip in shorter time

## Slide 2: Application Specific Integrated Circuit - ASIC
ASIC today are very complex electronic parts that perform complex tasks.
Manufacturing an ASIC chip is a major time and money consuming task. So it has to be faultless on first attempt.
Respin cost a lot of money and delay time to market.

## Slide 3: Stages in making a product
Characterization (with or without a client)
Architectural
Design + basic functional testing.
Producing first version (prototype).
Testing and corrections (using test plan).
Making beta version (to use with client).
Field testing & final fixes (with client).
Final version.

## Slide 4
Changes for chip design
Characterization (with or without a client)
Architectural
Design + module testing.
Full chip integration & verification.
Random testing.
RTL freeze -> Synthesize
Gate level (without/with timing)
Final version (tapeout).

## Slide 5: ASIC general structure
DUT2.v
DUT1.v
DUT0.v
Full chip
inputs
Full chip
outputs
ASIC is usually designed as Hardware blocks connected together.
Each block has input & output pins.
  Some blocks inputs are been driven by other blocks outputs.
Most ASIC has many operations modes which can be configured from the outside.
Configuration
inputs
ASIC block diagram

## Slide 6: Hardware modules – Design & verification
Test bench.v
(simulate board)
DUT.v
Design Under Test
Module DUT (
Input …,
Output …
);
Always @ (posedge clk or negedge rstb)
if (!rstb) …
else ….
Assign ….
.
.
endmodule
outputs
inputs
SIGNAL DRIVER
Simulate the full system inputs to our DUT
Test_in.txt
32’h12345678
32’h34567890
32’h567890ab
.
.
.
OUTPUTS CHECKER
Checks the DUT outputs against the DUT expected outputs
test_out.txt
32’h87654321
32’h09876543
32’hba098765
.
.
.
PASS/FAIL
Message to log file
The Data must be preraperd manually
We had to prepare the expected outcome
The machines are relative

## Slide 7: Automatic hardware verification environment
DUT.v
Design Under Test
inputs
outputs
SIGNAL DRIVER
Generate the input signals to our DUT
SEQUENCE DRIVER
INPUT
MONITOR
OUTPUT
MONITOR
CHECKER
(S/B)
Message to log file
SEQUENCE
LIBRARY
The Checker (score board). Prepare form the input signals, the expected output signals. Compare them and give a pass/fail massage.
The sequence driver. Send the scenarios to the design.
Signal Driver. Translate the high level scenarios (sequences) to low level signal, to be driven to the DUT.
The monitors (inputs & outputs). Read back the input/output signals and generate back a data structure to be transfer to the checker.
Active/Passive

## Slide 8: Full chip integration
DUT2.v
DUT1.v
DUT0.v
Full chip
inputs
Full chip
outputs
The chip integrator integrate all the chip’s modules into the chip’s top level file.
Configuration
inputs

## Slide 9: Full chip verification environment
Drivers for internal modules are no more needed. (passive mode)
DUT2.v
MON
MON
SB
SEQ
Driver
DUT1.v
MON
MON
SEQ
Driver
DUT0.v
MON
MON
SB
SEQ
Driver
Passive
Active
Full chip
inputs
Full chip
outputs
Configure driver
Cnf
SEQ
SB
Having an environment for each module means that the full chip integrator only have to combine those environments.
And we can have high level sequences controlling the low level
VIRTUAL
SEQUENCE DRIVER

## Slide 10: Random testing
DUT2.v
MON
MON
SB
SEQ
Driver
DUT1.v
MON
MON
SB
SEQ
Driver
DUT0.v
MON
MON
SB
SEQ
Driver
VIRTUAL
SEQUENCE DRIVER
Full chip
inputs
Full chip
outputs
At this stage we have a pretty big system and we let it go.
The system can now run scenarios on its own (Random).
At this point most of our test should PASS and we declare :
Configure driver
Cnf
SEQ
Top level score board
We keep building it to get cleaner and more readable results
RTL Freeze

## Slide 11: Synthesize & Gate level verification
DUT2.v
DUT1.v
DUT0.v
Full chip
inputs
Full chip
outputs
After the code is checked (for some stability) we do synthesis. This turn the code lines into electronic gates & flip-flops
Some of the inner signals will be lost in the process.
D
Q
CLK
rst
D
Q
CLK
rst

## Slide 12: Gate level testing
MON
MON
SB
SEQ
Driver
DUT1.v
MON
MON
SB
SEQ
Driver
DUT0.v
MON
MON
SB
SEQ
Driver
VIRTUAL
SEQUENCE DRIVER
Full chip
inputs
Full chip
outputs
When we lost some of the inner signals we can’t use the monitors & score boards.
But we now knew that those tests had passed in logic so if they fail now it is an electrical problem.
D
Q
CLK
rst
D
Q
CLK
rst
Configure driver
Cnf
SEQ
Top level score board

## Slide 13: Gate level with timing
Up till now we looked at the signals as rising & falling in 0 time. In the real would they don’t.
clock
input
output
clock
input
output
In real life it takes the gates & flip-flops to change their values.
DUT1.v
D
Q
CLK
rst
D
Q
CLK
rst

## Slide 14: Gate level with timing
We define the flip-flop’s ‘clock to Q’ & ‘delay time’ for the logic.
We define ‘setup time’ & ‘hold time’ that inputs must stand in .
clock
input
output
Setup time
Hold time
Clock to Q &
delay time
DUT1.v
D
Q
CLK
rst
D
Q
CLK
rst

## Slide 15: Gate level with timing testing
MON
Driver
DUT1.v
Driver
DUT0.v
MON
SEQ
Driver
VIRTUAL
SEQUENCE DRIVER
Full chip
inputs
Full chip
outputs
We run all the tests again. All the test that passed without timing HAVE to pass with timing.
This is the last check before production, any bug found later will force us to re-spin.
D
Q
CLK
rst
D
Q
CLK
rst
Configure driver
Cnf
SEQ
Top level score board

## Slide 16
And …
Tape out
We send the design to production and hope for the best 